## Slide 1
All-Inclusive but Practical Multivariate Stochastic Forecasting for Electric Utility Portfolio
Background Facts
Stochastic Variable Generation
Resource Dispatch Optimization
Hedge Analysis
5. Daily Volatility & Spike Model
Daily historical data
- On-peak Load
- Off-peak Load
- Hydro generations
- Natural gas prices
- Power prices
[i – viii]
External LT forecasts in monthly granularity.
- Econometric load forecasts
- Metrological hydro forecasts
[i – v, viii – x]
Market settlement price data, such as forward and option prices [x]
Hourly congestion price shapes at multiple (10 - 30) nodes. [i – viii]
Wind data is independent and does not fit AR model.
[iii, v, viii]
Generation by thermal resources are determined economically based on prices and its capability. Need to take into account of future outage schedules set by utilities.
[iv, x]
DATA
[objective]
METHODS
[packages::function]
Grubb’s Outlier Test
Applied twice before and after decomposition. [outliers::grubbs.test]
Fourier series
LOESS [stats::loess]
Subset Regression
Weekly shapes and auto-regression factors are captured here. [leaps::regsubsets]
Hierarchical Clustering
Collinear variables are taken out of the main AR model and derived later using predictive models. [stats::hclust]
Multivariate Gaussian Model
Héston Model
ARIMA(1,2,0)
If an external LT forecast does not exist, it is derived from trend and seasonality components (step 3).
Seasonal Block Bootstrapping
Multiple Regression
Denton Disaggregation
Monthly LT forecasts (step 4) need to be disaggregated into daily time series, before combining with daily noise (step 5). [modified ‘tempdisagg’]
Objective
The wholesale power market is the most volatile market of all commodity markets.
Consumers pay a relatively flat electricity rate to utilities. This means that utilities need to manage market risks.
Some utilities set annual budgets probabilistically, meaning that the chance of insolvency given a specified cash reserve must be below a certain threshold.
Many utilities hedge risk by trading forwards or options.
Random Forest/GLM
Collinear or dependent variables (step 2) are derived using predictive models. All trees of RF are utilized (with Bayesian inference) to capture variability. [caret::train, stats::glm, randomForest::randomForest]
Logical Dispatch Calculation
Given resource unit specifications, determine the optimal economic dispatch schedule for each stochastic iteration.
Scheduled Tasks
On Demand
Temporal Hierarchical Reconciliation
Generated stochastic data is reconciled so that means match with market expectations.
Ultimately, we want some Risk Metrics that guide us to avert risks.
AUTHOR: Eina Ooka
Sr. Structure and Pricing Analyst
The Energy Authority
eooka@teainc.org
https://github.com/einaooka/useR2016
(See this link for references)
Portfolio Analysis through R-Shiny App
A user can interactively analyze stochastic scenarios and run hypothetical forward or option trades through shiny app. [shiny, shinhdashboard, rhandsontable]
Report through Rmarkdown
Hedge analysis can be made into a html report through the app. [knitr]
Quantify market risk that utilities are exposed to, through stochastic simulation of loads, resources and market prices.
Portray appropriate tail risk with 1,000 or more stochastic iterations.
Capture the following data characteristics:
  Autocorrelation
  Heteroscedasticity
  Seasonal and weekly shape
  Mutivariate cross-correlation and non-linear dependency
  Non-normal distributions
  Extreme peaks and drops
  Negative prices
  Max and min caps
  Reasonable long-term distributions
  Consistency with market and utility expectations
STEPS
Time Series Decomposition
Simulated Time Series
Historical vs. Simulated
Non-linear Multivariate Dependency
Energy Balance
Shiny App
Resource Dispatch
1. Data Scraping
2. Collinearity and Dependency Detection
3. Multiplicative Decomposition
Outlier + Seasonality x Trend x Noise
4. Long-Term Stochastic Forecasting
6. Disaggregation and Combination
7. Judgmental Adjustment
8. Markov Chain Model
11. Resource Dispatch
12. Cash Flow Aggregation
14. Portfolio Optimization
9. Predictive Modeling
10. Hourly-Shape Analysis
13. Scenario & Hedge Analysis
Regional Hydro Generation (aMW)
K-Means Clustering [stats::kmeans]
Multinominal Logistic Regression
Each day is categorized to a particular hourly shape based on daily averages. [nnet::multinom]
Utility A